## Slide 1
Micro-asphalt treatment involves 1 or 2 thin layers of a bitumen/ aggregate slurry being spread over the existing road surface. This seals the surface, preventing water from getting into cracks.
Description
New road surface
Life-expired road
Highway condition
Structurally sound, with early signs of defect
Similarly to surface dressing, micro-asphalt can restore a road to near-new condition, extending it’s life by up to 10 years. It is relatively cheap and quick to deliver, at 3-4x cheaper than resurfacing and the road can reopen in 30-60 minutes.
Benefits
Best suited to lower-traffic roads, such as residential roads, which are structurally sound but have early signs of defect.
Where appropriate
Light
Heavy
Traffic level
Less durable than surface dressing, best suited for low-speed/residential roads
Crack/pothole
Full road
Size of repair
Full-width of carriageway and best value over larger distances
Which roads are suited for this treatment?
Key features of the treatment
£5-8 per m2
Delivery time
Treatment sets very quickly so road can be reopened for traffic within 30-60 minutes
Carbon
Low emissions as layer of material is thin and laid cold.
Weather
Needs dry weather during application.
Micro Asphalt

## Slide 2
Involves spraying a sticky bitumen binder onto the road, before a layer of stone chippings is rolled in. This seals the road surface to prevent water getting into cracks and causing damage.
Description
New road surface
Life-expired road
Highway condition
Structurally sound, with early signs of defect
Can restore a road to near-new condition, extending its life by up to 10 years. It is also relatively cheap and quick to deliver, at 5x cheaper than resurfacing and 1km covered in 2 hours.
Benefits
Mid-life treatment for all types of road (urban/rural) and traffic-levels (heavy/light) that are structurally sound but have early signs of defect. May be challenges in very-urban settings, due to chippings being flicked up when speed limit is exceeded.
Where appropriate
Light
Heavy
Traffic level
All traffic levels
Crack/pothole
Full road
Size of repair
Full-width of carriageway and best value over larger distances
Which roads are suited for this treatment?
Key features of the treatment
£3-5 per m2
Delivery time
Road closed for 1 day. Temporary speed limit of 20mph for 1-2 days while chippings embed into surface.
Carbon
Much lower than full resurfacing due to use of approximately 75% less bitumen and aggregate.
Weather
Needs dry weather during application.
Surface dressing

## Slide 3
Existing surface is pulverised before being mixed with new bitumen and aggregate. This is then re-laid into a new base layer. This is left overnight to harden before a surface dressing is applied
Description
New road surface
Life-expired road
Highway condition
Near end-of-life roads with large levels of deterioration.
Reduces carbon impact by cutting waste and doesn’t require the heating of materials. Extends the road life by 10-20 years.
Benefits
Best suited for large schemes and end-of-life roads with extensive defects. It requires specialised equipment and is less suitable for urban areas due to dust and challenges working around utilities.
Where appropriate
Light
Heavy
Traffic level
All traffic levels
Crack/pothole
Full road
Size of repair
Full-width of carriageway and best value over larger distances
Which roads are suited for this treatment?
Key features of the treatment
£18-45 per m2
Delivery time
Road typically closed for 1-2 days during application as base needs to be left overnight before dressing applied.
Carbon
Low emissions as recycles existing material, reduces transport needs and is laid cold.
Weather
Needs dry weather during application.
In-situ recycling

## Slide 4
The top layer (30-50mm) of a worn-out road is removed using machinery. It’s then replaced with a new, smooth layer of asphalt which is then compacted to create a durable and even surface.
Description
New road surface
Life-expired road
Highway condition
Near end-of-life roads with large levels of deterioration.
Restores life-expired road to good condition, improving grip, smoothness, and longevity. Avoids ongoing reactive maintenance to fix recurring potholes.
Benefits
Life-expired roads, suitable for all traffic levels.
Where appropriate
Light
Heavy
Traffic level
All traffic levels
Crack/pothole
Full road
Size of repair
Full-width of carriageway and best value over larger distances
Which roads are suited for this treatment?
Key features of the treatment
£25-35 per m2
Delivery time
Can take up to 1 day to allow new surface to cure.
Carbon
Higher than other preventative treatments due to need to replace and transport large quantity of material.
Weather
Needs dry weather during application.
Full resurfacing

## Slide 5
A specialised adhesive sealant is applied to cracks in the road to prevent the infiltration of water that may cause damage if left untreated.
Description
New road surface
Life-expired road
Highway condition
Early stage of the highway lifecycle when defects first begin to emerge.
Fast to apply and more cost-effective than repairing potholes. Seals early signs of defect to prevent water getting in and causing more damage.
Benefits
Roads (all traffic levels) that are showing early signs of wear-and-tear.
Where appropriate
Light
Heavy
Traffic level
All traffic levels
Crack/pothole
Full road
Size of repair
Small defects
Which roads are suited for this treatment?
Key features of the treatment
Low but highly variable (see note)
Delivery time
Fast and road can reopen almost immediately.
Carbon
Low – material usage is minimal compared to other treatments.
Weather
Typically done in spring or autumn to avoid seasonal variation in cracks (e.g. expansion in winter).
Crack sealing

## Slide 6
This is a rapid repair method that uses a high-pressure machine to apply a mix of emulsion and aggregate directly into a pothole. Some machines use compressed air or a flame to clear and dry the pothole, before a coat of emulsion is applied to help the new material bond with the existing surface. Finally, new material is sprayed into the hole to create a new, smooth surface.
Description
This technique is fast to deliver, allowing roads to re-open quickly. Trucks can navigate hard-to-reach areas, allowing repairs on rural roads where a hot patch repair may be challenging.
Benefits
Delivering rapid repairs on roads where a quick re-opening is required.
Where appropriate
Key features of the treatment
Delivery time
Rapid delivery, road typically reopened within an hour. 100-200 repairs per shift.
Carbon
Dependent on delivery approach, but higher than cold-lay approach due to use of materials and heating.
Weather
Suitable for all seasons.
Spray injection patching
Location
Most suitable for low-medium traffic levels. Can be intermediate solution in higher-traffic areas, but repair is often not as durable as hot asphalt patching due to the weaker bond with the existing surface.
Equipment
Specialist spray injection machine needed.

## Slide 7
Durable method for fixing potholes. First, the pothole is cleaned, and the edges may be squared for better adhesion. A sticky binder coat is applied, then hot asphalt is poured in layers and compacted to create a smooth, solid surface. Once it cools (usually within an hour), the repaired area is ready for traffic, providing a long-lasting fix.
Description
This technique is highly versatile – it is quick to deliver, suitable for all locations, relatively long-lasting, and can be delivered in all seasons.
Benefits
Delivering a long-lasting repair on a high-traffic area.
Where appropriate
Key features of the treatment
Delivery time
Varies depending on equipment used – c.10-30 minutes per pothole, allowing 250m2 per day.
Carbon
Dependent on delivery approach, but higher than cold-lay approach due to use of materials and heating.
Weather
Suitable for all seasons.
Hot asphalt patching
Location
Suitable for all locations and traffic levels.
Equipment
Specialist equipment needed – binder sprayer, chipping spreader, roller.

## Slide 8
Similar to the “hot patching” approach, but rather than excavating existing material, heat is applied to soften the surface around the damaged area. New binder and asphalt is applied and compacted. This aims to deliver a very strong bond between the old and new material, eliminating any weak points where water could permeate the surface.
Description
Delivers a hard-wearing repair due to strength of bond with existing surface and absence of joint between old and new material. Can be more aesthetically pleasing than hot asphalt patching, due to blend with existing surface.
Benefits
Medium and high traffic areas where a durable and seamless repair is desirable.
Where appropriate
Key features of the treatment
Delivery time
Approximately 30 minutes per repair.
Carbon
Energy required to heat surface (gas or infra-red), but existing material is recycled rather than excavated.
Weather
Unsuitable for delivery during rain and very cold weather.
Thermal repair patching
Location
Suitable for high-traffic areas, due to strong seal.
Equipment
Infra-red heater or gas burner required

## Slide 9
There are different types of cold lay, but the traditional approach is for pre-mixed asphalt to be laid into the pothole and compacted with a roller or vehicle tires. No heating is required, making it a quick fix. This is typically a temporary, emergency fix and can be applied quickly in wet conditions.
Description
This technique is quick to deliver and can be delivered in all seasons, and at all times of day.
Benefits
Temporary emergency repairs until a longer-term solution can be delivered.
Where appropriate
Key features of the treatment
Delivery time
Very quick and can be driven on immediately.
Carbon
Lower than hot application of material.
Weather
Suitable for all seasons, can be applied in wet conditions.
Cold lay material
Location
Relatively low durability of material means this best suited to low-traffic areas. However, can be a helpful emergency repair in high-traffic areas, to “make-safe” an urgent issue.
Equipment
No specialist equipment needed.